Maidment (1993): Handbook of Hydrology
Table 4.4.1: Selection and Computation Sequence for Estimating the Energy (Needed?) for Evaporation

1	Are local measurements of net radiation (Rn in MJ m-2 day-1) available?
YES:	(i)	Divide by λ [Eq. (4.2.1)] to give Rn in mm day-1.
(ii)	Go to 5(a).
NO:	Continue with 2(a).

2(a)	Are local records of fractional cloud cover (n/N) available?
YES:	Go to 3(a).
NO:	Continue with 2(b).

2(b)	Local records of sunshine hours (n) available?
YES:	(i)	Compute (n/N); N from Eq. (4.4.1).
(ii)	Go to 3(a).
NO:	Continue with 2(c).

2(c)	Can n or n/N be estimated from regional records?
YES:	(i)	Proceed as 2(a) or 2(b).
(ii)	Recognize increased uncertainty in (n/N).
(iii)	Go to 3(a).
NO:	Select pan- or temperature-based evaporation estimate.

3(a)	Local measurements of solar radiation (St in MJ m-2 day-1) available?
YES:	(i)	Divide by λ [Eq. (4.2.1)] to give water equivalent.
(ii)	Go to 3(c).
NO:	Continue with 3(b).

3(b)	Locally calibrated Angstrom coefficients (as, bs) available?
YES:	Select as and bs from available values.
NO:	Set as = 0.25; bs = 0.50.
THEN:	(i)	Obtain value of extraterrestrial radiation (S0) from Eq. (4.4.4).
(ii)	Compute St from Eq. (4.2.6).
(iii)	Continue with 3(c).

3(c)	Local measurements of land cover albedo (α) available?
YES:	Select value of α from available measurements.
NO:	Estimate α using Table 4.2.2.
THEN:	(i)	Compute net solar radiation from Eq. (4.2.5).
(ii)	Continue with 4(a).

4(a)	Locally calibrated emissivity coefficients [ae, be; Eq. (4.2.8)] available?
YES:	Select ae and be from available values.
NO:	Set ae = 0.34; be = –0.14.
THEN:	Continue with 4(b).

4(b)	Measurements of dew point temperature available?
YES:	(i)	Obtain vapor pressure ed at dew point temperature from Eq. (4.2.2) or Table	4.2.1.
(ii)	Compute ε' from Eq. (4.2.8).
(iii)	Go to 4(d).
NO:	Continue with 4(c).

4(c)	Measurements of minimum air temperature available?
YES:	(i)	Set dew point to minimum temperature; obtain ed from Eq. (4.2.2) or Table	4.2.1.
(ii)	Compute ε' from Eq. (4.2.8).
NO:	Compute ε' from Eq. (4.2.9).
THEN:	Continue with 4(d).

4(d)	Locally calibrated cloudiness coefficients [ac, bc; Eq. (4.2.10)] available?
YES:	Select ac and bc from available values.
NO:	Set ac = 1.35; bc = –0.35 in arid areas
or ac = 1.00; bc = 0.00 in humid areas.
THEN:	(i)	Compute clear sky solar radiation St0 as the value given by Eq. (4.2.6) with	(n/N) set to zero.
(ii)	Compute the cloudiness factor (f) from Eq. (4.2.10).
(iii)	Compute net long-wave radiation from Eq. (4.2.7).
(iv)	Compute net radiation from Eq. (4.2.13).
(v)	Continue with 5(a).

5(a)	Estimate of available energy for open water surface required?
YES:	Go to 5(b).
NO:	Go to 5(c).

5(b)	Data to estimate advected energy [Ah; Eq. (4.2.20)] available?
YES:	(i)	Compute Ah from Eq. (4.2.20).
(ii)	Energy available for evaporation A = Rn + Ah.
NO:	Energy available for evaporation A = Rn.
THEN:	Energy estimation complete.

5(c)	Measurements or data to estimate soil heat flux G available?
YES:	(i)	Obtain G from measurements, or estimate from Eq. (4.2.18) or (4.2.19).
(ii)	Energy available for evaporation A = Rn – G.
NO:	Energy available for evaporation A = Rn.
THEN:	Energy estimation complete.

The equations:

(4.2.1)	%lambda = 2.501 - 0.002361 T_s MJ kg-1	Ts: water surface temperature (°C)
(4.2.2)	e_s = 0.6108 exp left( {17.27 T} over {237.3 + T} right) kPa	T: air temperature (°C)
(4.2.5)	S_n = S_t ( 1 - %alpha ) MJ m-2 day-1	St: global radiation (MJ day-1)
(4.2.6)	S_t = left( a_s + b_s n over N right) S_0 MJ m-2 day-1	as, bs: Angstrom coefficients
n: sunshine hours per day (h)
N: total day length (h)
(4.2.7)	L_n = L_i - L_o = - f %varepsilon' %sigma ( T + 273.2 )^4 MJ m-2 day-1	Lo: outgoing lw radiation
Li: incoming lw radiation
f: cloudiness correction factor
ε': net emissivity between	atmosphere & ground
(4.2.8)	%varepsilon' = a_e + b_e sqrt{ e_d }
(4.2.9)	%varepsilon' -0.02 + 0.261 exp ( -7.77 times 10^{-4} T^2 )
(4.2.10)	f = a_c S_t over S_{ t0 } + b_c
(4.2.13)	R_n = S_n + L_n MJ m-2 day-1
(4.2.18)	G = 0.38 ( T_{day2} - T_{day1} ) MJ m-2 day-1
(4.2.19)	G = 0.14 ( T_{month2} - T_{month1} ) MJ m-2 month-1
(4.2.20)	A_h = %rho_w c_w ( q_i T_i - q_0 T_0 + P T_p ) = 4.19 times 10{ -3 } ( q_i T_i - q_0 T_0 + P T_p ) MJ m-2
(4.4.1)	N = 24 over %pi %omega_s
(4.4.4)	S_0 = 15.392 d_r ( %omega_s sin %varphi sin %delta + cos %varphi cos %delta sin %omega_s ) mm day-1

The tables:

Tab. 4.2.2: Albedos for different land cover classes
Land cover class	Albedo
Open water	0.08
Tall forest	0.11 – 0.16
Tall farm crops (e.g., sugarcane)	0.15 – 0.20
Cereal crops (e.g., wheat)	0.20 – 0.26
Short farm crops (e.g., sugar beet)	0.20 – 0.26
Grass and pasture	0.20 – 0.26
Bare soil	0.10 (wet) – 0.35 (dry)
Snow and ice	0.20 (old) – 0.80 (new)